What I’ve been up to...
- Not much time to go into depth
- But, I’ll start at the beginning
- Arduino: founded in 2008
- Microcontrollers exploded from there
  - Unique features of the Arduino:
    - Cheap!!
    - Open source!!
    - Simple programming language and environment (written in language similar to C++, and in fact can utilize C++ and C libraries

---
Other advantages
- Only a single process is run at a time: no overhead of an operating system, etc.
- Easy to build and add shields, attach to other boards, etc.
- Lend themselves VERY easy to experimental control, and are very accurate as noted and tested previously noted in “Arduino: A low-cost multipurpose lab equipment” (Alessandro D’Ausilio, 2012).

---
Teensy microcontrollers
- Basically, the same thing, with a few unique features
- Has a library built on top of the Arduino library (i.e. can use Arduino functions, plus many extras!)
- We utilize the 3.2 in particular
- Similar number of channels, but capable of true analog output (instead of PWM)
- Faster processor (potentially more accuracy): 72 vs 16 MHz
- All pins have interrupt capability (we don’t utilize this here)
- Special, added libraries on top of the standard Arduino libraries

---
Teensy libraries
- Key functions: IntervalTimer → generates interrupts at microsecond time scale; can utilize 4 at a time
- Audio library: 44.1 kHz library for playing and synthesizing tones – super easy to use, and can be used concomitantly with other interval timers
- Plug-and-play add-ons: e.g. prop-shield serves as an easy amplifier: just solder on, and you are good to go
- Like Arduino, capable of interacting with serial peripheral interfaces, like the ADNS-9800

---
ADNS-9800
- Originally a gaming sensor
- Board created recently by Jack Enterprises (https://www.tindie.com/products/jkicklighter/adns-9800-laser-motion-sensor/)
- 12000 FPS frame rate, up to 8200 counts per inch (compare to ~ 125 fps max, maybe 1000, and far fewer counts per inch)
- 16 bit storage: don’t have to poll as often, so the sensors won’t saturate

---
ADNS-9800
- Simple SPI interface
- Our Mark expanded the included code into a library, so it is easy to start sensors, clear, and read from motion burst registers and others using his code instead of diving into the nitty gritty (back in 2014...)
- Downsides: wiring the sensors kind of sucks

---
Figure 2 (audio and motor schematic)

---
Figure 3
Data collected from the device is temporally VERY accurate, only slightly biased

---
 Figure 4
Tone puff: also very accurate

---
Conclusion
- Use these!
- Excellent temporal resolution; not as high-level as MATLAB: less jitter/competing processes
- Easy to set up
- Should be easy to integrate into ViRMeN (sp?), if anyone wants a project?

---
Revisions to the original manuscript

---
Issues: do PV cells increase their firing before MSNs?
Do CHI interneurons peak later than MSNs?
Also, how do we know that percent change in speed is different for three cell types?

---
FSI
MSN
CHI

---
Criticism: why not combine everything into a single model and thereby
make inferences?

---
Reviewer comment: argue that the change in proportion of pairs coactive vs distance is different for all three cell types, but demonstrate no statistics

---
Now, beginning a “network” analysis
- Mentioned over the summer, several papers have reported that neurons form clusters that are spatially biased
- What do we see when we use the same methodology? (meta k-means)
  - 1st, randomly select chunk of data
  - Run k-means 100 times with “correlation” as distance metric
  - Randomly select different chunk of data
  - Make histogram: # of times that each pair together
  - Choose cutoff value that maximizes # of clusters

---
Summary statistics

---
Make sure we are converging on same clusters

---
Summary statistics

---
Next steps
Keep going down this path? Then, see whether or not clustering